## Slide 1: PLC & SCADA
RATNESH VERMA
1509720042
EE(3rd Year)

## Slide 2: What is AUTOMATION
Making products under the control of computers and
programmable controllers is known as automation.
Manufacturing assembly lines as well as stand alone machine
tools and robotic devices fall into this category.
It is delegation of human control functions to technical equipment for increasing the productivity, quality, and increasing the safety in working conditions thereby reducing the manpower and cost.

## Slide 3: INSUSTRIAL AUTOMATION
Now a days, every small and large industry employ automation.
In manual control, an operator periodically reads the process and adjusts the input accordingly. Quite hectic!
In automation control, measurements and adjustments are done automatically on a continuous basis. Quite convenient!

## Slide 4: Types of Control Systems used in INDUSTRIAL AUTOMATION
PID controller based control system
PLC based control system
DCS based control system
PC based control system

## Slide 5: PLC(Programmable Logic Controller)
It is microprocessor based solid state/industrial computer that perform discrete or sequential logic.
It was developed to replace mechanical relays, timers, counters.
The early PLC’s were used to reduce the changeover time, wiring/re-wiring.
PLC works on 24V DC and I/O devices that are directly connected to PLC also works on 24V DC.
To connect it with AC devices we use relay and transistor

## Slide 6: Brands of PLC’s
Panasonic
Allen Bradley
Delta
Omron
Siemense
Keyence
Schnieder
Mitshubishi

## Slide 7: Different types of programmable controller

## Slide 8: Types of PLC
Fixed/Compact type
Expansion is not possible
Fixed number of I/O ports
Memory up to 2kb
Maximum 248 I/O ports are possible
Modular type
Expansion is possible
Serial expansion
Memory up to 32kb
Maximum 2048 I/O ports are possible
Rack type
Expansion is possible
Parallel expansion
Maximum 16000 I/O ports are possible
Memory up to 2mb

## Slide 9: Architecture of a PLC
BLOCK DIAGRAM
INPUT DEVICES
PLC
OUTPUT DEVICES
POWER
SUPPY
MEMORY
INTERFACE
(24V DC, 120V AC)
(Toggle or Push buttons, proximity or pressure sensors)
(Displays & Monitors)
(External memory module)
(SCADA or HMI)

## Slide 10: PROGRAMMING the PLC
Programming language used:
LADDER language- The programming can be done with simple contacts that simulate the opening and closing of relays, counters, timers, shift registers and other math operations.

## Slide 11: START- STOP LOGIC:
START:
hardware software
NO-
NC-
STOP: NO-
NC-

## Slide 12: Software for the Programing of Allen Bradley PLC
RSLinx Classic( Driver Software)
RSLogix 500 English(Programing Software)
RS Logix Emulate 500(Simulation Software)

## Slide 13: Advantages
Reliability in operation.
Flexibility in control and programming techniques.
Online offline modifications.
Small physical size, shorter project time.
In house simulation and testing of project.
Speed of operation.
Ease of maintenance and troubleshooting.
Ability to communicate and networking with computer system in plant.
Documentation and security.
Designed to work in all types of industrial conditions.

## Slide 14: Applications
Material Handling
Packaging Applications
General Industrial Machinery
Printing
Food and Beverage
Pharmaceutical
Water Wastewater / SCADA
Clutch/Brake control
Position Control - Pick-and-place / Conveyor

## Slide 15: SCADA
Supervisory Control And Data Acquisition
It is a software through which we can create visualization of any industrial process.
Earlier, PLC’s were programmed, download the program in it and it used to run for years
The problem- no one knew what’s happening inside the PLC.
Solution= PLC+SCADA

## Slide 16: FEATURES OF SCADA
Alarm
Real time trend and historical trend view
Security
Device connectivity

## Slide 17: SCADA Software
Wonderware- Intouch
Rockwell- RS view32
Siemens- winCC
GE- Intellation

## Slide 18: Application of SCADA

## Slide 19: Application of SCADA

## Slide 20: Bottle Filling

## Slide 21: THANK YOU !!!